Simple DC Circuits (open):
Here is perhaps the simplest circuit we could build. In this case the light bulb is the “load” in the circuit, controlled by a “single pole, single throw” (SPST) switch. (More about switches later.)
    Materials that have a large supply of free electrons in their atomic structure are referred to as conductors (e.g. copper, gold.) Conversely, materials with relatively few free electrons are called insulators (e.g. wood, rubber.) If the electromotive potential is great enough, just about anything can become a conductor, even the air in the sky (in the case of lightning.)

---
Simple DC Circuits: (closed)
Electricity flows from a source, where there is the greatest concentration of electrons (positive pole) to the place with a relatively lower concentration of electrons (negative pole, often also referred to as “ground”) through the path of least resistance.
DC (Direct Current) circuits harness the power of the electrical current flowing from a positive source, energizing a load of some kind as it passes through it to ground.

---
Simple DC Circuits: (short!)
- Always make sure there is a load of some kind on the circuit. A path through a conductor directly from source to ground is called a short circuit (very bad.) It will cause the power source to over-heat and die. In this case it would cause the battery to get very hot and die. If this happens with AC current in your home it can cause catastrophic fires.

---
Series and Parallel:
When connected “in series”, DC voltage sources are added. In the above example, two AA batteries (1.5 volts each) wired in series supply 3 volts to the circuit. (1.5 + 1.5 = 3.)
When connected “in parallel”, batteries' voltages are unaffected, but the current (measured in amperes) is increased. In the above example, two AA batteries (1.5 volts each) wired in parallel supply 1.5 volts to the circuit, but can do so for a longer time than a single battery alone.

---
Series and Parallel load:
The concept of being “in series” or “parallel” also applies to electrical components which are wired as the load of the circuit.

---
Some Definitions:
– The name for the property of having a “positive” and “negative” polar
    orientation is called “polarity.” Magnetic polarity and electrical
   polarity are inextricably linked.
- When a magnetic field is moved through a coil of wire, it causes
   electrons to move through the wire (electricity) in a process called
   “induction.” The moving magnetic field “induces” electrical current.
- Direct Current (DC) occurs when electrons flow in one direction
   continuously along a conductor. This is the kind of current obtained
   from batteries and is generally safe to work with at low voltages, and
   is the main kind of current we will be working with in our circuit
   constructions.
- Alternating Current(AC) occurs when the direction or polarity of the
  current alternates direction. AC is better suited for transmission through
   long distance power lines. Household (wall plug) current in North
   America delivers 110-115 volts, alternating at 60 times a second (60
   Hz). A wire carrying AC will induce a current in nearby wire.
- “Wall current” (110-115 VAC) is a dangerous, potentially life-threatening
   energy source. Do not use it in the circuits you build without the advice
   and oversight of faculty and staff who can assure the work is done safely.

---
Some Definitions:
– Electricity (electrons flowing through a circuit) has two principle
   properties: voltage and current.
- Electromotive potential (symbol: V, or sometimes the more archaic E)
   is the difference in potential energy between two points in a circuit. It is
   measured in units called volts (after Alessandro Volta, inventor of the
   battery.) In the metaphor of water and plumbing often used to visualize
   electrical charge flowing in a circuit, voltage would be thought of as water
   pressure.
- Current: (symbol: I for “intensité”) Current is the rate of flow, or volume
   of electrical charge through a circuit. The unit of measure is the
   ampere, usually shortened to “amp” (after French physicist André-
   Marie Ampère.) It's a measure of how many electrons go past a given
   point in a circuit per second. (In the water metaphor, current can be
   thought of as the diameter of the pipe.)
- Power (symbol: W) Volts and amps multiplied together equals the total
   amount of electrical power in the circuit, measured in units called watts
   (after James Watt, Scottish inventor and engineer.)
- Resistance (symbol: Ω -Greek letter for omega) Also called impedance,
   is measured in units called ohms (after German physicist, Georg Ohm.)

---
Thinking about current:
The famous “water metaphor”
Electrical components called “resistors” slow down the flow of electrons, and are essential for controlling the flow of electricity in a circuit. The electrical energy lost when current goes through a resistor is transformed into heat. The property of impedance (resistance) in a resistor is measured in units called ohms. In the metaphor, it's represented by pinching the water pipe.
The water pressure (measured between two points) is a metaphor for electromotive potential, measured in units called volts.
The diameter of the pipe (or volume of water flowing) is a metaphor for current. It is measured in units called amperes (amps.) One ampere = a volume of one coulomb per second. -A coulomb is a measure of charge equal to 6.24 * 1018 electrons.

---
...Except that it's all really backwards!
Benjamin Franklin made several important contributions to the study of electricity, among them was the theory that the two types of charge were not two different “electrical fluids”, but rather, resulted from a single “fluid.” He also came up with the labels of “positive” and “negative” for the different types of charge. He decided that the “fluid” flowing was “positive.” Almost a hundred years later when the electron was discovered, it was learned that Franklin got it backwards. To this day, (and in this class) “conventional current” flow is described as flowing from positive to negative, even though electrons (negatively charged particles) flow towards a positive pole.

---
Prefixes:
These prefixes are universally used to scale units in science and engineering:
When abbreviating a unit with a prefix, the symbol for the unit follows the prefix without space. Be careful about upper-case and lower-case letters (especially m and M.) 1mW is a milliwatt, or one-thousandth of a watt, but 1MW is a megawatt (one million watts.) The unit name is only capitalized when it is abbreviated. For example, in describing cycles-per-second we use hertz and kilohertz, but Hz and kHz.

---
Working with Multimeters
As you can imagine there are many
different meters for measuring things. (“Ohmmeters” for measuring resistance, “Voltmeters” for measuring voltage, etc.) They come in analog and digital flavors.
Probably the most useful tool we will be using to understand what's going on in our circuits is the digital multimeter (DMM). You should all get one if you are serious about working with electronics.
As its name implies, it is a collection of multiple types of meters in one handheld device. Especially useful in our first circuits are the voltmeter (with the dashed line indicating dc current) and the ohmmeter (in different ranges by the “omega” symbol.)

---
Meter “ranges”
Multimeters are available that are “auto-ranging”, but we will be using the more economical manually-ranged meters. This means you will be manually selecting both the type of meter and the range within which you will be measuring.
Start by selecting the range you think is closest to the value you will be measuring. In this example, I'm measuring something I think is around 6 volts, so I start in the range of 0 – 20 volts. I'm measuring dc current, so I select the range in the area next to the “V” with a dashed line. (The “V” with the wavy line is volts of ac current.)

---
Meter “ranges”
If I move dial to the 0 – 200 volt range, notice what happens:
The meter is displaying the same value, but it moves over one decimal place to make room for a sign (+ or -) and larger, three digit number. -And notice I'm losing some resolution (the hundredths place) in the process. Selecting the range closest to the value you are measuring will give you the most precise measurement (most decimal places.)

---
Meter “ranges”
If I move dial to the 0 – 1000 volt range, notice what happens:
The meter is displaying the same value, but it moves over one decimal place to make room for a sign (+ or -) and larger, four digit number.
-And notice I'm losing some resolution (the tenths place) in the process.

---
Meter “ranges”
The range below 0 – 20 volts has a small letter “m” indicating that it is a range measuring millivolts (thousandths of a volt.)
Note: 0 – 2000 thousandths of a volt
is the same as measuring 0 – 2 volts.
Since the voltage we are measuring is 5.71 volts, the meter displays a numeral 1 at the left of the display. This is what the display looks like when it is measuring a value that is “out of range.” If you see it, just move the dial to a larger range. (Or check that you are not trying to measure the wrong units, like volts instead of ohms.)
Lastly, be sure to turn the meter off when you are finished to save battery life.